Centripetal acceleration and tangential velocity estimation:

Acceleration in the NED earth frame is:
{bold{A}}_i^e = {bold{A}}^e - g_0 {bold hat{z}}_e	(1)

Where {bold A}_i^e is the inertial acceleration measurement, {bold A}^e is acceleration with respect to the earth frame, and g_0 {bold hat z}_e is the acceleration due to gravity. If the vehicle is stationary with respect to the earth frame, the accelerometers will indicate upward acceleration of -g_0 {bold hat z}_e since bold hat{ z } points downward in the NED frame.

In a coordinated turn the centripetal acceleration is:
{bold{A}}^e = {bold %omega}^e times {bold V}^e	(2)

where {bold{%omega }}^e is the turn rate, {bold{V}}^e is the tangential velocity and the body-frame acceleration is:
{bold A}_i^b = R_e^b [ {bold %omega}^e times {bold V}^e - g_0 {bold hat z}_e ]	(3)

g_0 {bold hat z}_e = {bold A}_i^e - {bold %omega}^e times {bold V}^e	(4)

Now, assuming { bold V }^e = V { bold hat x }_b^e solve equation 4 for the velocity {bold V}^e , then plug it back in to find the current estimate of g_0 {bold hat z}_e .

{bold %omega}^e times {bold V}^e = {bold A}_i^e - g_0 {bold hat z}_e = { bold A }^e	(5)

{bold %omega}^e times (V {R_b^e bold hat x}_b) = {bold A}_i^e - g_0 {bold hat z}_e	(6)

But {bold %omega}^e = %omega_z^e {bold hat z}_e :
matrix { V %omega_z^e [{bold hat z}_e times ( {R_b^e bold hat x}_b)] # {}={} # {bold A}_i^e - g_0 {bold hat z}_e ## V %omega_z^e bold hat c # {}={} # {bold A}_i^e - g_0 {bold hat z}_e ## V %omega_z^e # {}={} # ldline{bold A}_i^e - g_0 {bold hat z}_e rdline }	(7)

The centripetal acceleration estimate is therefore:

ldline{bold A}_i^e - g_0 {bold hat z}_e rdline [{bold hat z}_e times ( {R_b^e bold hat x}_b)]	(8)

in the earth frame.

Thrust vector estimation:
In a multirotor aircraft, the thrust vector is -T { bold hat z }^b along the body z axis. Let {bold T}^e = R_b^e ( -T {bold hat z}^b ) represent the thrust in the earth frame. In a steady-state turn, the thrust component in the earth horizontal plane will equal the drag+centripetal force: {bold F}_h(bold V) = { bold T }_x^e + { bold T }_y^e . The radial component of force counters centripetal force and the tangential component counters drag. Assuming tangential acceleration is zero: instead of { bold V }^e = V { bold hat x }_b (assuming zero slip) in equation 5, solve directly for { bold V }^e where the rate of rotation {bold %omega}^e is the rate of rotation of the thrust vector. The direction of thrust in the earth frame is %theta = atan2( {bold T}_y^e, {bold T}_x^e ) and ldline {bold %omega}^e rdline = dot %theta .

{bold A}^e = { bold %omega }^e times { bold V }^e	(9)

The estimated tangential velocity is then:

V_t = ldline {bold A}^e rdline over dot %theta	(10)

on 270 deg/sec turntable:
with orientation roll 44 deg, pitch 2 deg, estimated tangential velocity is 0.56 +.02 -.01 m/sec
measured omega is 4.8 +/-0.4 rad/sec
with orientation roll 25 deg, pitch -38 deg, estimated tangential velocity is 0.52 +/-.02 m/sec
measured omega is 4.8 +/-0.4 rad/sec
with R=0.125 m, ground truth is 0.59 m/sec
centrip_thrust_r14 with mag compensation:
with orientation roll 44 deg, pitch 1 deg, estimated tangential velocity is
regarding tangential velocity estimate centripetal_0.tV: it appears to be useful only when omegaE is on the order of 1 rad/sec or larger.
the 3D magnetic vector roll/pitch error corrections look good when applied if thrust vector omegaE > 0.5 rad/sec
plots of mag vector in earth frame look pretty good. modified code to also log estG in earth frame for comparison